## Slide 1: Further Expansions
Module 2.06 from BlackHat Training
Trainer: Colin O’Flynn

## Slide 2: Overview
Background to Development
Synchronous Sampling
Connecting CW To Target Device
  Voltage Translators
  Serial IO
  Programming the AVR
Software
  Overview of two parts
  Overview of project files
  About scripting
  About special scripts
Capture Software
Analysis Software
FPGA Project

## Slide 3: Objectives
Introduce ChipWhisperer System
Comparison of ChipWhisperer System to Existing
Learn important details of connecting hardware
Learn software methodology

## Slide 4: A Simple Block Diagram…

## Slide 5: Clock Routing Inside the FPGA

## Slide 6: Clock Routing GUI

## Slide 7: Input Clock Limits
Limits inside Spartan 6 FPGA used by ChipWhisperer
Generally ~5MHz LOWER limit on clock frequencies!
Can use external PLL instead to improve this

## Slide 8: Input Clock Limits
Can get lower frequencies if you are careful (requires changes to FPGA design!):

## Slide 9: Output Clock Limits
Can get lower frequencies if you are careful (requires changes to FPGA design!):

## Slide 10: Physical Connections

## Slide 11: FPGA-Controlled Target-IO Lines
Purpose: Medium speed digital IO, controlled by FPGA project.
Specs: 4 IO lines, bi-directional including open-drain support (e.g. I2C). FPGA can choose to drive lines using push-pull (faster IO) or open-drain.
Examples:
Interface for Target communication
Trigger Lines

## Slide 12: FPGA-Controlled High-Speed Lines
Purpose: Very high speed digital IO for clocks, controlled by FPGA.
Specs: 2 IO lines, bi-directional but must set direction from FPGA (e.g. another line sets if input or output). VERY FAST slew rate, be careful of ringing.
Examples:
Clock Input from Target
Clock Output to Target
Glitch Output

## Slide 13: Data Directories
If you didn’t save a project before capture:
default-data-dir
If you saved a project before capture:
$projectname$_data

## Slide 14: Wave Format
[Trace Config]
numTraces = 5000
format = native
numPoints = 3000
prefix = 2014.06.13-20.12.56_
date = 2014-06-13 20:12:56
scopeSampleRate = 0
notes = ""
scopeName = unknown
scopeXUnits = 0
targetSW = unknown
targetHW = unknown
scopeYUnits = 0
[Aux Data 0000 - Partition Randomly (debug)]
round = 0
filename = 2014.06.13-20.12.56_PartitionRandDebug_aux_0000.npy
[Aux Data 0001 - Partition Randomly (debug)]
round = 0
filename = 2014.06.13-20.12.56_PartitionRandDebug_aux_0001.npy

## Slide 15: Wave Format
Wave files SAVED during capture
Project file made by linking all wave files into one project file
If capture crashes hopefully no or little data lost…
Determines how many files to write
Traces/File = NoTraces/CaptureSegments

## Slide 16: Scripting Some Files

## Slide 17: Scripting Some Files
Open the file training_material\copy_paste\script_analyzer.py

## Slide 18: Scripting some Files
Copy to your Virtual Machine
Run the File

## Slide 19: Like Magic!

## Slide 20: Open a Project File…
#User commands here
print "***** Starting User Script *****"
ana.openProject("/home/chipwhisperer/example_traces/avr/avr-vcc-5k-normal.cwp")
pe()
print "***** Ending User Script *****"

## Slide 21: Run some GUI Commands…
#User commands here
print "***** Starting User Script *****"
ana.openProject("/home/chipwhisperer/example_traces/avr/avr-vcc-5k-normal.cwp")
pe()
ana.setParameter(['Generic Settings', 'Result Collection', 'Input Trace Plot', 'Trace Range', (0, 10)])
ana.setParameter(['Generic Settings', 'Result Collection', 'Input Trace Plot', 'Redraw', None])
print "***** Ending User Script *****"

## Slide 22: The Attack Script

## Slide 23: Preprocessing Modules

## Slide 24: More Scripting Examples…

## Slide 25: Capture Software Architecture

## Slide 26: FPGA Project Generation
#!/bin/sh
../../../../openadc/hdl/makeise/./makeise.py ztex_rev2_1.11c_ise.in ztex_rev2_1.11c_ise/ztex_rev2_1.11c_ise.xise
#
# Input file for OpenADC-MakeISE for the ChipWhisperer-CaptureRev2 Hardware
#
# OpenADC-MakeISE is a method of making ISE Project files automatically, and will eventually
# be extended to include command-line design flows. This saves the issue of dealing with changes
# in project files being added to git, especially if using different versions of ISE.
#
# WARNING: Everything is CASE SENSITIVE
#
[ISE Configuration]
#Generate project configuration
#You can specify any parameter here which will override the input file 'defaults'
InputFile = ise_verilog_template.xise.in
Version = 14.4
Device Family = Spartan6
Package = ftg256
Device = xc6slx25
Speed Grade = -3
Verilog Include Directories = ../../../hdl|../../../../../openadc/hdl/hdl
#This is needed to allow the partial bitstream files to be generated successfully
Other Map Command Line Options = -convert_bram8

## Slide 27: FPGA Project Generation
[Setup File]
ZTEX
UART_CLK = 30000000
MAX_SAMPLES = 24573
FAST_FTDI
NOBUFG_ADCCLK
CLOCK_ADVANCED
SYSTEM_CLK = 30000000
TARG_UART_BAUD = 38400
HW_TYPE = 3
HW_VER = 0
#ENABLE_RECONFIG
#ENABLE_I2C

## Slide 28: ChipWhisperer Main FPGA Project

## Slide 29: Generating Bitstreams + Partial Files
Bitstream location specified in GUI
  Date printed on start-up, ensure it’s finding your new file!
  Will have to unplug/replug CW first to clear old bitstream

## Slide 30: Generating Bitstreams + Partial Files
If you want glitch generation, need to run the generate_reconfig_dicts.py script in chipwhisperer\hardware\capture\chipwhisperer-rev2\hdl
  WARNING: Takes a long time
  Then copy s6lx25-glitchwidth.p & s6lx25-glitchoffset.p to chipwhisperer\software\chipwhisperer\capture\scopes\cw-partial-files
  CW-Capture uses timestamps to confirm partial files & bitstream are consistent (~within 8 hours). If not the partial reconfiguration is disabled & message printed

## Slide 31
This training content is Copyright © NewAE Technology Inc. 2016. ChipWhisperer is a trademark of NewAE Technology Inc., registered in the United States of America and Europe. See terms and conditions at ChipWhisperer.io